## Slide 1
Community based DDOS protection and why Peering / IX's are an important mitigation tool
John Brown, CISSP, CP-AMEL

## Slide 2
Security Classification / Pictures of Slides
This presentation is marked as TLP:CLEAR
What is TLP (Traffic Light Protocol) ?
See https://www.first.org/tlp/
Taking pictures of slides is PERMITTED
Please try to keep other peoples faces out of the pictures
The entire presentation will be available via email, just ask me
TLP:CLEAR

## Slide 3
AGENDA
Introduction / Who is John Brown?
Review of DDOS and Mitigation Methods
What is new in UTRS Version 2.0
Questions and Answers

## Slide 4
About Me
John Brown, CISSP, CP-AMEL
Senior Security Evangelist at Team Cymru
35+ years as software and network engineer
Have built Internet networks on 3 continents
Past owner of a regional ISP business, ran it for 17 years
Ran ICANN’s L-Root DNS server, one of 13 critical DNS servers
Passionate about helping ISP’s improve their networks
Past Mikrotik Authorized Instructor (MT-CNA, MT-CRE, MT-CINE)
Commercial Multi-Engine Pilot
When not working, I enjoy flying airplanes.
I can be reached at: jbrown@cymru.com

## Slide 5
AGENDA
Introduction / Who is John Brown?
Review of DDOS and Mitigation Methods
What is new in UTRS Version 2.0
Questions and Answers

## Slide 6: What is DDOS
DDOS = Distributed Denial of Service.
  It is an attack against one or more network resources designed to prevent that resource from providing normal services.
DDOS can be via an amplification attack, or the attack can be at the application layer.
  Malicious actor sends a small flow of special packets towards a service that has a large response. Examples: Recursive DNS servers, NTP, CHARGEN and others.

## Slide 7: Business as Usual – clients reaching server via Network Operators
AS65540
AS64499
AS64450
AS64498
AS65537
AS64497
AS65538
AS64451
AS65536
AS65539
www.$.com

## Slide 8: DDoS Effect – knocking down services
AS65540
AS64499
AS64450
AS64498
AS65537
AS64497
AS65538
AS64451
AS65536
AS65539
www.$.com

## Slide 9: How to mitigate, traditional methods.
Traditional mitigation methods
  Build a ACL (Access Control List) on your border router.
    Doesn’t scale well across multiple border routers
    Doesn’t scale well when there are hundreds or thousands of source IP’s
    Your transit link is already congested, thus impacting more of your net.
    Ask your transit provider to filter, attack is still successful.

## Slide 10: How to mitigate, the RTBH method
RTBH (Remote Triggered BlackHole)
  A special BGP session with your transit provider or peering partner
    Using BGP to signal (tell them) your peer that you want them to drop traffic TO a specific address on your network.
    Pushes the problem upstream. Your peer / transit is now absorbing the DDOS traffic. Hope their pipes are big enough to do that !!
    Works pretty good, you must build BGP sessions with each transit or peering partner. May not scale well..

## Slide 11: SOS – RTBH Request
AS65540
AS64497
AS65538
AS64451
AS65536
AS65539
www.$.com
AS64499
AS64450
AS64498
AS65537
Remote Trigger Black Hole

## Slide 12: How to mitigate, the Scrubbing method
Subscribe to a “Scrubbing Service”
  A third-party now announces your routes via BGP.
  Traffic is redirected to the scrubbing service provider.
  They scrub / filter out the unwanted traffic.
  The “Good / Clean” traffic is sent to you via a GRE tunnel.
  Increase latency, Reduction in control over your announcements
  Works well for application layer attacks

## Slide 13: Who is the Victim ??
Who is the Victim in a DDOS ???
  The compromised host / Bot that is part of the BotNet
  The ISP for the Bot.
  Transit / Peering providers in between the Bot and the Target
  The ISP providing connectivity to the Target
  The Target itself.
  5 different categories of victims.

## Slide 14
What if……..
We could tell more than 1000 networks to drop traffic we didn’t want
With only ONE SIMPLE BGP announcement!!

## Slide 15: How to mitigate, the UTRS method
UTRS == Unwanted Traffic Removal Service
  Uses RTBH methods, but at scale
  Team Cymru as a trusted partner, receives your request to drop traffic
  TC validates the request
  TC then sends the request out to the thousands of other UTRS members
  Nearly instantly your traffic is being dropped as far upstream as possible
  Leverages features from u/RPF (Unicast Reverse Path Filtering)
  BCP 38

## Slide 16: UTRS
AS65540
AS64497
AS65538
AS64451
AS65536
AS65539
www.$.com
AS64499
AS64450
AS64498
AS65537
Remote Trigger Black Hole
UTRS Servers

## Slide 17: What is new UTRS 2.0
Based on community feedback, Team Cymru has added new features:
  Increase the prefix size from IPv4 /32 to IPv4 /25
  Redundant Route Servers, geographically diverse, better peering
  IPv6 support. We will now accept IPv6 up to a /49
  Flowspec
  RPKI Validation

## Slide 18: What is new UTRS 2.0
Increase the prefix size from IPv4 /32 to IPv4 /25
  By allowing larger IPv4 prefixes we help prevent “carpet bombing”
  Aligns better with route acceptance boundaries

## Slide 19: What is new UTRS 2.0
Redundant Route Servers
  Many partners require two or more peering locations.
  Partners also require geographically diverse locations
  Increases redundancy, which increases reliability of service.
  Existing UTRS 1.0 users will need to migrate to new peer IP’s
  Email coming soon to coordinate the migration.

## Slide 20: What is new UTRS 2.0
IPv6 support
  Most DDOS has been via IPv4 networks
  IPv6 is growing and in some parts of the world will be dominate soon.
  We now accept IPv6 prefixes up to a /49

## Slide 21: What is new UTRS 2.0
Flowspec
  Allows for a more refined “surgical” removal of unwanted traffic
  Flowspec rules MUST
    Have a destination CIDR in the rule
    Set action to DROP
  Flowspec rules MAY
    provide SRC/DST port (explicit, no ranges),
    Protocol (TCP, UDP, etc)

## Slide 22: What is new UTRS 2.0
RPKI Validation
  We will validate based on RIR information

## Slide 23: THE ASK
Please help spread the word about UTRS and how this NO-COST service can be used to stop malicious traffic and become an Internet Hero.
https://www.team-cymru.com/utrs

## Slide 24
Thank you!
Become a Nimbus Partner
https://team-cymru.com/community-services/nimbus-threat-monitor/
Join our Community DDOS Mitigation Project
https://team-cymru.com/community-services/utrs/
Connect with Team Cymru on Social Media
@teamcymru
Email: outreach@cymru.com