## Slide 1: When Satellite is All You Have: Watching the Internet from 550 ms
Daniel Perdices; Gianluca Perna; Martino Trevisan; Danilo Giordano; Marco Mellia
24 April 2024
Perdices, D., Perna, G., Trevisan, M., Giordano, D., & Mellia, M. When satellite is all you have: watching the internet from 550 ms. In Proceedings of the 22nd ACM Internet Measurement Conference. Doi: 10.1145/3517745.3561432

## Slide 2: Satellite Communication (SatCom) in a Nutshell
Customers connect via a GEO (Geostationary Earth Orbit) satellite network
  More than 36.000 km from Earth
  More than 550 ms RTT for Internet access
  Equipped with multiple directional antennas
    Each manages a transmission beam aimed at to a specific region on the earth
Customers connect to the SatCom network via customer-premises equipment (CPE)
  manages link and access protocols
  acts as a Performance Enhancing Proxy (PEP)
  sends data via the satellite to the ground station using a UDP tunnel (L4 Proxy)
The Ground Station on the provider-premises receive the customer’s data traffic
  uses a PEP to break the connection and access the Internet
> 550 ms RTT
36.000 km

## Slide 3: Satellite Communication (SatCom) in a Nutshell
Customers connect via a GEO (Geostationary Earth Orbit) satellite network
  More than 36.000 km from Earth
  More than 550 ms RTT for Internet access
  Equipped with multiple directional antennas
    Each manages a transmission beam aimed at to a specific region on the earth
Customers connect to the SatCom network via customer-premises equipment (CPE)
  manages link and access protocols
  acts as a Performance Enhancing Proxy (PEP)
  sends data via the satellite to the ground station using a UDP tunnel (L4 Proxy)
The Ground Station on the provider-premises receive the customer’s data traffic
  uses a PEP to break the connection and access the Internet
> 550 ms RTT
36.000 km
SatCom breaks TCP connections to speed-up the communication
Customer-premises SatCom equipment impersonates the the destination server by
  Breaking 3-way handshake  Send data with no delay
  Buffering TCP data and send it to the ground-station  uplink speed
Ground station establishes a new TCP connection with the actual destination server
  Speed regulated by the download rate of the customer device  Preserve PEP buffer
  Work as Network Address Translation (NAT) box, DNS resolver*, and Quality of Service (QoS) schedulers
*default but customer may change it

## Slide 4: The Questions
How does customers’ traffic look like?
How much does customers consume?
What customers consume?
Which performance customers get?

## Slide 5: Measurement Setup
Tens k customers
20 countries Max 5 Mbit/s Up Up to 100 Mbit/s Down
February – April 2022
34.4 Billions flows
4.3 PB of client traffic
  Process traffic in real-time
      100+ statistics computed at the end of the flow
  Implements DN-Hunter
      To Track DNS conversations
      To tag the network flows with the FQDN
5
c_ip | c_port | c_pkts | c_bytes | s_ip | s_port | s_pkts | s_bytes | Protocol
12.132.54.94* | 1197 | 1 | 18938 | 87.250.137.92 | 443 | 1 | 992221 | HTTP
Tstat
*Client IP address is anonymized
TLS/SNI
Facebook.com
FQDN
Facebook.com
DN-Hunter

## Slide 6: Measurement Setup
Tens k customers
20 countries Max 5 Mbit/s Up Up to 100 Mbit/s Down
February – April 2022
34.4 Billions flows
4.3 PB of client traffic
  Process traffic in real-time
      100+ statistics computed at the end of the flow
  Implements DN-Hunter
      To Track DNS conversations
      To tag the network flows with the FQDN
6
c_ip | c_port | c_pkts | c_bytes | s_ip | s_port | s_pkts | s_bytes | Protocol
12.132.54.94* | 1197 | 1 | 18938 | 87.250.137.92 | 443 | 1 | 992221 | HTTP
Tstat
*Client IP address is anonymized
TLS/SNI
Facebook.com
FQDN
Facebook.com
DN-Hunter
When | FQDN
Current | facebook.com, fbcdn.com
Before | fbstatic-a.akamaihd.net
“A name indicates what we seek.
An address indicates where it is.
A route indicates how we get there.”
*Full list at https://dl.acm.org/doi/10.1145/3517745.3561432
Regexp* | Service
facebook.com, fbcdn.com, ˆfbstatic-[a-z].akamaihd.net$ | Facebook
netflix.com, nflxvideo.net | Netflix
Jon Postel – RFC 791

## Slide 7: How does customers’ traffic look like?

## Slide 8: Customers country and aggregate volume
% of total volume and customers per country
African countries have high number of customers and high volume per customer
  Approximately 600 MB/day
European countries with high number of clients but low volume per customer
  Approximately 170 MB/day
African countries may share the connection with several end-users
European countries only use it when they are forced to do so

## Slide 9: How daily pattern looks like?
% of volume per hour w.r.t. peak time
  All aligned to UTC – different only for Spain and South Africa
Clear daily patterns, but differences between continents
  High usage during daylight hours in Africa, low usage in Europe
  Peak time for both peak time is around 20-21

## Slide 10: How much does customers consume?

## Slide 11: How much customers consume?
250
Focus on active clients only
Clients with > 250 flows/day
Complementary Cumulative Distribution Function (CCDF) of the daily number of flows per customer
  Europe
    High percentage of inactive customers
  Africa
    Most customers are active
    Produce more flows than European customers
    Internet access may be shared by several devices in the same household/business/internet café

## Slide 12: How much customers consume?
Complementary Cumulative Distribution Function (CCDF) of the daily download volume per active customer
African customers download more data than European customers
Smaller increase in terms of volume difference
Heavy hitters (download > 10GB/day)
  In Congo 8% while in Spain 4%
This behavior impacts the
  Congestion on the SatCom link
  The per-customer cost of the SatCom operator in terms of volume

## Slide 13: What customers consume?

## Slide 14: What users consume
Identify domain names
  QUIC and TLS SNI
  DNS queries
  HTTP hostname
Service identification
  List of services and associated set of domains (regexes)*
.netflix. .nflxext. .nflximg. .nflxvideo. .nflxso.
Netflix
assets.nflxext.com
*Full list at https://dl.acm.org/doi/10.1145/3517745.3561432

## Slide 15: What service customers consume?
Service popularity per country for active customers
  % of customers accessing each service
Focus on the service the customer wants to contact
  Remove services that can be contacted during other visits, e.g., YouTube
Chat
  Whatsapp has the highest popularity
  Snapchat is 2nd. Highly popular in Congo and Ireland
Social
  Instagram and TikTok have similar popularity
    TikTok only 4 to 7 < Instagram
Audio/Video streaming
  Are more popular in Europe than in Africa except for South Africa

## Slide 16: What category of service customers consume?
Volume per service category per country for active customers
  All services: social buttons, tracking cookies, etc., consume little volume compared to the actual service
Chat
  Median European consumes < 10 MB/day
  Median African consumes > 250 MB/day
    Top-5 % of the heaviest customers consume > 2 GB/day!
Social
  Median European consumes < 30 MB/day
  Median African consumes > 300 MB/day in Congo
Audio/Video streaming
  Similar volume in all countries
  But different services!
    Free YouTube in Africa, paid streaming services in Europe
Higher Chat and Social volume may be
related to the sharing of SatCom connection

## Slide 17: Which performance customers get?

## Slide 18: Which Performance customers get? (Satellite RTT)
Distribution of Satellite RTT during
  Peak time (13:00 – 20:00)
  Night (off-peak 2:00 – 5:00)
Satellite RTT: time from the customer terminal to the ground station
RTT min at 550 ms and > 2 s
Spain and Nigeria best RTT
  Favorable location
Congo highly differ between peak and night
  Possible congestion problem
Ireland no difference between peak and night hours, but poor performance
  Possible location problem

## Slide 19: Which Performance customers get? (Satellite RTT and Beam utilization)
Distribution of Satellite RTT versus beam utilization during the peak time
  Beam utilization is normalized based on the maximum utilization of all beams to avoid disclosing the actual per-beam utilization
Congo and Ireland suffer high delay
  Independent of the beam utilization
Congestion is due to the PEP not the beam
  Due to beam resource allocation
   The complexity of SatCom is higher than expected!

## Slide 20: Which Performance customers get? (DNS & RTT based)
DNS popularity and response time per DNS resolver
  % of active customers
Most customers set their own DNS
  Regardless of the lowest Response Time
  Especially in Africa
In Africa, customers often use Nigerian and Chinese DNS
  High impact of the ground segment

## Slide 21: Which Performance customers get? (DNS & RTT based)
Impact of DNS resolver on the ground RTT
Ground RTT: time from the ground station to the actual server
Same service, different CDN based on DNS resolver
   Potentially leading to very high ground RTT

## Slide 22: Conclusion

## Slide 23: Conclusion & Future Work
Conclusion
Different customer patterns among countries
  African countries could share Internet access
  European countries may use it only if forced to do so
  European countries are more likely to use satellite at night or during leisure time
  African countries use the satellite to a significant extent throughout the day
The satellite RTT changes not only based on beam congestion
DNS resolution plays a key role in selecting the closest server in the CDN
Future work
Using IPv6 to study the phenomenon of connection sharing in Africa
Investigate how QUIC and other UDP-based protocols evolve over time